## Slide 1: HTTP, Wireshark, and Digital Forensics
Notes: https://www.youtube.com/watch?v=6G3qm60dfA8&ab_channel=PrashantThombre

## Slide 2: Overview
Observe HTTP traffic with curl
Is understanding HTTP enough for forensic investigations?
  Open Systems Interconnection Model (OSI)
Exam HTTP traffics with Wireshark
  Three-way handshake (TCP)
  Communication (HTTP request/response)
  Close connection (TCP)

## Slide 3: Observe HTTP traffic

## Slide 4: What is HTTP?
HTTP stands for hypertext transfer protocol and is used to transfer data across the Web
HTTP Request
HTTP Response

## Slide 5: Create a simple html page to be observed in wireshark
change html folder permission

## Slide 6
service apache2 stop service apache2 restart
Create a simple webpage, named basic.html, and
Put it in the folder /var/www/html
Start web service
Show the webpage
Notes: <!DOCTYPE html>
<html>
<body>
<h1>My First Heading</h1>
<p>My first paragraph.</p>
</body>
</html>
https://www.w3schools.com/html/tryit.asp?filename=tryhtml_basic_document

## Slide 7
cURL (pronounced 'curl')
A command-line tool
Open source
Transferring data
Support many network protocols
-v: verbose, show headers

## Slide 8: Is understanding HTTP enough for forensic investigations?

## Slide 9: Importance of understanding underneath of HTTP
Many layers (OSI Model) are defined to form computer networks
  HTTP is one protocol at an application layer
Forensic investigation focus on all layer
  Malware analysis
  Attack analysis
  File extraction
The OSI Model (Open Systems Interconnection Model)
  is a conceptual framework used to describe the functions of a networking system.

## Slide 10
HTTP Request
HTTP Response

## Slide 11
Segment:
Data
Packet
Frame
bit
Notes: https://www.youtube.com/watch?v=-6Uoku-M6oY

## Slide 12
Clear browser cache
Notes: rm -r ~/.cache/mozilla/firefox/*default*
wireshark -i lo -k -w ~/traffic/basic.log
curl 127.0.0.1/basic.html

## Slide 13
Notes: wireshark ~/traffic/basic.log

## Slide 14: Three-way handshake
No. 1, 2, and 3

## Slide 15
SYN (seq =m)
SYN (seq =n) + ACK (m+1)
ACK (n+1)
CLOSED
LISTEN
SYN-RECEIVED
ESTABLISHED
CLOSED
SYN-SEND
ESTABLISHED
Port 57338
Port 80
Sequence #:
  the byte number of the first byte of data in the TCP packet sent
  beginning at random # or 0 (relative seq#)
ACKnowledge #: the sequence number of the next byte the receiver expects to receive.
  Seq # + size of packet + 1
  The receiver ack'ing sequence number x acknowledges receipt of all data bytes less than (but not including) byte number x
  +1 for SYN
n, m are in bytes
choose init seq num, m
received SYNACK
indicates server is live;
send ACK;
client state
Server state
1
2
3
Notes: https://www.freecodecamp.org/news/an-introduction-to-http-understanding-the-open-systems-interconnection-model-9dd06233d30e/
https://www.geeksforgeeks.org/tcp-3-way-handshake-process/
https://www.geeksforgeeks.org/tcp-connection-termination/

## Slide 16
Client:
I am sending seq # m
I will use the seq # m to indicate the byte number of the first byte of data in the TCP packet sent
m
1

## Slide 17
Server:
I’ve received your seq # m
I expect to receive your next seq# m+ 1
I’m sending seq # n and I will use it to indicate the byte number of the first byte of data in the TCP packet I am sending
n
m+ 1
2

## Slide 18
Client:
OK. I am sending seq # m+ 1 as you requested
I expect to receive seq # n +1
n +1
m+ 1
3

## Slide 19: HTTP request protocol
No. 4

## Slide 20
SYN (seq =0)
SYN (seq =0) , ACK (0+1)
(seq =1) , ACK (0+1)
Port 57338
Port 80
handshake
Transfer
(seq =1) , ACK (0+1), TCP len=t1
(seq =1) , ACK (1+t1), TCP len=0
http request/TCP
(seq =1) , ACK (1+t1), TCP len=t2
http response/TCP
(seq =1+t1) , ACK (1+t2), TCP len=0
1
2
3
5
7
4
6

## Slide 21
SYN (seq =0)
SYN (seq =0) , ACK (0+1)
(seq =1) , ACK (0+1)
Port 57338
Port 80
handshake
Transfer
(seq =1) , ACK (0+1), TCP len=83
(seq =1) , ACK (1+83), TCP len=0
http request/TCP
(seq =1) , ACK (1+83), TCP len=352
http response/TCP
1
2
3
5
(seq =1+83) , ACK (1+352), TCP len=0
7
TCP length t1=83
TCP length t2=352
4
6

## Slide 22
Show http request
4

## Slide 23
Show TCP segment 4
Show TCP payload
4
Show http request

## Slide 24
Show IP packet 4
4
Show http request

## Slide 25
Ethernet Frame 4
lo interface is not associated with a hardware network interface (it's a virtual loopback interface), it does not have an Ethernet hardware address (MAC address).
Show Ethernet 802.3
ARP (0x0806)
4
Show http request

## Slide 26: HTTP response protocol
No. 5 and 6

## Slide 27
Server ACKnowledges the request
ACK 84 =1+ TCP length
5

## Slide 28
6
Server send HTTP response head
HTTP head

## Slide 29
Server send HTTP response data (simple.html)
6
simple.html

## Slide 30
PSH: data must be transmitted promptly to the receiver
6
Server send HTTP response data (simple.html)
TCP

## Slide 31
7
Client sends TCP acknowledgement

## Slide 32: TCP Close connection

## Slide 33
FIN_WAIT_2
CLOSE_WAIT
FIN, ACK=84+1, seq=353
ACK=353+1
ACK=84+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
FIN_WAIT_1
FIN, ACK=353, seq=84
can no longer
send but can
receive data
client state
server state
ESTAB
ESTAB
Port 57338
Port 80
8
9
10

## Slide 34
8

## Slide 35
9

## Slide 36
10